General Fire Precautions

The Regulatory Reform (Fire Safety) Order 2005 (RRO) applies to caravan sites and is enforced by the Fire Authority.

Article 9 of the RRO states that the responsible person must make a suitable and sufficient assessment of the risks to which relevant persons are exposed for the purpose of identifying the “general fire precautions” he/she needs to take to comply with the requirements and prohibitions imposed on him/her by the Order.

General Fire Precautions cover measures such as:

(1) the means of escape in case of fire;

(2) the means of securing the means of escape, including fire-fighting arrangements;

(3) the means for giving warning in case of fire; and

(4) the management of measures (1)-(3) above, including staff training, fire drills and testing/maintenance of fire-fighting equipment and fire alarms.

It would be an expected outcome of a fire risk assessment thet the following or equally effective measures should be in place for caravan and camping sites:

- Fire points should be established so that no caravan or site building is more than 30m from a fire point.  They should be housed in a weatherproof structure, easily accessible and clearly and conspicuously marked “FIRE POINT”.

- Where water standpipes are provided and there is a water supply of sufficient pressure and flow to project a jet of water approximately 5m from the nozzle, such water standpipes should be situated  at each fire point.  There should also be a reel that complies with British Standard 5306 Part 1, with a hose not less than 30m long, having a means of connection to a water standpipe (preferably a screw thread connection) with a water supply of sufficient pressure and terminating in a small hand control nozzle.  Hoses should be housed in a box painted red and marked “HOSE REEL”.

- Where standpipes are not provided but there is a water supply of sufficient pressure and flow, fire hydrants should be installed within 100m of every caravan standing.  Hydrants should conform to British Standard 750.  Access to hydrants and other water supplies should not be obstructed or obscured.

- Where standpipes are not provided or the water pressure or flow is not sufficient, each fire point should be provided with water extinguishers (2 x 9 litre).

- A means of raising the alarm in the event of a fire should be provided at each fire point.  This could be by means of a manually operated sounder eg, metal triangle with a striker, gong or hand operated siren.  The advice of the fire authority should be sought on an appropriate system.

- All alarms and fire fighting equipment should be installed, tested and maintained in working order by a competent person and be available for inspection by, or on behalf of, the enforcing authority.  A logbook should be kept to record all tests and any remedial action.

- All equipment susceptible to damage by frost should be suitably protected.

- A clearly written and conspicuous notice should be provided and maintained at each fire point to indicate the action to be taken in case of fire and the location of the nearest telephone.  This notice should include the following:

“On discovering a fire:

- Ensure the caravan or site building involved is evacuated

- Raise the alarm

- Call the fire brigade (the nearest telephone is sited ………………)

- Tackle the fire using the fire fighting equipment provided, if safe to do so.

- It is in the interest of all occupiers of this site to be familiar with the above routine and the method of operating the fire alarm and fire fighting equipment.

- Long grass and vegetation should be cut at frequent and regular intervals where necessary to prevent it becoming a fire hazard to caravans, buildings or other installations on the site.  Any such cuttings should be removed from the vicinity of caravans.  The space beneath and between caravans should not be used for the storage of combustible materials.

- An immediately accessible telephone should be available on the site for calling the emergency services.  A notice by the telephone should include the address of the site.